## Slide 1: Fluoroscopy
James, armin, nate, pete, Sean, Hanro

## Slide 2: Medical Relevance
Developed in late 19th Century
  Popularized in 1960s
Uses
  Surgery
  Cardiology
Decline in use
  Exposure based health concerns
  Lack of Training
How can we combat these issues?
Fluoroscopy

## Slide 3: Demonstration!
Volunteer?

## Slide 4: Mechanical Design

## Slide 5: Bed Mechanism
Rack and Pinion
  Small tooth number
    Effective 3D-Printing
    Less resolution
  Small pitch diameter
    Efficient use of space
    High start-up torque / overpowers static friction
Friction fit to remove need for external support

## Slide 6: C-Arm Mechanism
Bearing
  Reduces friction in rotational movement
Motor Fitting
  Tolerancing issues
Set Screw System
  Preferably more user friendly
Torque Capabilities
  Low mass of C-arm = Low rotational inertia

## Slide 7: Electrical Design

## Slide 8: Micro Controller
An Arduino Uno was chosen due to it being readily available and easy to use by others should they want to replicate this project
MSEduino could also be used but not readily available to everyone and difficult to use at times (especially when uploading code)

## Slide 9: Power Distribution
A 9v battery is used as the power source for the circuit.
Motors are rated for 6v so a power supply module is used to step down the voltage to 5v while keeping current high.

## Slide 10: Motor Control
Two 6v DC motors are used to actuate both the C-Arm and bed.
The DC motors are controlled with a MX1508 motor controller to control direction.
DC motors vs Stepper motors for C arm

## Slide 11: Software Design

## Slide 12: Arduino Software
In terms of pin outs 4 digital IO pins are required for control of the motor controller and 2 analog pins are used to input the joystick position to the Arduino
Joystick Y and X directions control each respective motors
Each joystick has movement threshold close to extreme positions

## Slide 13
2 motor functions are called within the loop that set the directions of each motor
Directions are changed by setting respective direction pins to high or low

## Slide 14
Joystick x and y values are read from the analog pins
Motor direction functions are called within the main loop when the joystick position in either the y or x axis pass the minimum and maximum thresholds

## Slide 15: ACCELEROMETER
Issues with accelerometer
What if it worked?
  Accelerometer communication
  Position Based Actuation
  Image Processing based on Position Data

## Slide 16: Effective Prototype?
Good
  Mechanical shape and design
  General functionality
  Scalable
  Intuitive actuator interface (joystick)
Bad
  No transducer for C-arm translation
    Poor set screw design
  Non-steady actuator performance
    No feedback mechanism (accelerometer non-functioning)
  No full-stop locking mechanism + poor resolution
    Gears have wiggle

## Slide 17: Project Lessons
Start early and plan for mistakes
  Accelerometer issues
Design for tolerancing
  Size and shape
Seak most efficient design
  Lowest Infill to support prototype
  Unnecessary material usage
Use what you already have
  Don’t reinvent the wheel
  Tried to create our own motor controller - we already have one!

## Slide 18: Thankyou

## Slide 19: Questions?